## Slide 1: Transport NBI Design Team Update
Italo Busi
Daniel King

## Slide 2: Transport NBI DT
IETF is developing a set of YANG Models that could be used for Transport NBI
  How existing IETF YANG Models can be used for transport networks?
  Are there any gaps in the existing IETF YANG Models?
TNBI DT is currently looking at
  Use Cases
  Analysis of how existing IETF YANG models can be used to support these Use Cases
Working method
  Mailing list
  Weekly conference calls on Wednesday at 3:00pm CET
  GitHub: https://github.com/danielkinguk/transport-nbi

## Slide 3: Use Cases
Use Case I-D updated:
  https://tools.ietf.org/html/draft-tnbidt-ccamp-transport-nbi-use-cases-02
Added
  Protection scenarios for Use Case 1: Single-domain with single-layer
Next steps
  Use Case 3: Multi-domain with single-layer
  Complete Use Case 1
  Use Case 2: Single-domain with multi-layer
  Use Case 4: Multi-domain and multi-layer

## Slide 4: Analysis – Use Case 1
Analysis I-D for Use Case 1 published:
  https://tools.ietf.org/html/draft-tnbidt-ccamp-transport-nbi-analysis-uc1-00
Currently Covers
  ODU Abstract Topology example (white topology)
  ODU Transit Service example
  Detailed JSON code examples – validated against YANG models
Next Steps
  Reformat JSON code to fit into IETF I-D template
  Align JSON code examples to latest YANG models
  Complete analysis of Use Case 1
  Analysis of protection scenarios
  Start analysis of Use Case 3

## Slide 5: Feedbacks to IETF WGs
Assumptions to be validated by TEAS WG
  Applicability of TEAS YANG models to ACTN MPI interface
  Use of the TE Tunnel model to setup Tunnel Segments
  MDSC configures the labels (TSs) on the access link based on the label set information it can get by the PNC TE Topology
Feedbacks to TEAS WG
  How to use the TE Tunnel model to configure Tunnel Segments – on-going discussion
  Use of node-id and link-tp-id in case of unnumbered explicit-route-object in TE Tunnel model
  Add information about the label set in TE Topology and TE Tunnel models
  Detailed syntax fixes as identified during the validation of the example JSON code against YANG models
Feedbacks to CCAMP WG
  Under preparation

## Slide 6: Use Case 1
S1
S2
S3
S4
S5
S6
S7
S8
Transport domain
C-R1
C-R2
C-R3
IP domain
C-R5
C-R4
MDSC
IP PNC
Client Controller
Transport PNC
CMI (initially out of scope)
IP MPI
(out of scope)
Transport MPI
(in the scope)

## Slide 7: Abstract White Topology @MPI
ODU Abstract
Topology
@MPI
C-R1
C-R2
C-R3
C-R5
C-R4
S3-1
S6-2
S3
S6
S1
S2
S4
S5
S7
S8
PNC exports as abstract topology at MPI: TE nodes (since the white topology abstraction is used, they represents physical nodes) , TE links (between TE nodes) , access-links (facing transport border nodes) , transport border nodes and link termination points (LTPs) (e.g.S3-1 and S6-2)
The IP domain (reported here in the blue rectangle) is not part of the topology exported. They are included in this picture just to show the end points of the access links.
The topology model provides «external-domain» container that alows the MDSC to glue togather the different domains to create E2E abstract multi-domain topology.
S6-1

## Slide 8: ODU2 Tunnel Setup
Abstract
Topology
@MPI
C-R1
C-R2
C-R3
C-R5
C-R4
MDSC should request Transport PNC to setup an ODU2 Tunnel (Segment) between S3-1 and S6-2
Ingress and egress points are indicated in the explicit-route-objects of the primary path:
  First element of the explicit-route-objects refers to S3-1 LTP
  Last element of the explicit-route-objects refers to S6-2 LTP
  The tunnel to be setup is a segment tunnel, source and destination of the E2E tunnel
  information is belonging to customer side.
S3-1
S6-2
S3
S6
S1
S2
S4
S5
S7
S8

## Slide 9: ODU2 Connection: TEAS Tunnel Model Instantiation
To be added

## Slide 10: Next Steps
Socialise I-Ds outside of IETF at other SDOs, these include:
  ONF
  MEF