## Slide 1: NBI DT 11/01/2017
Meeting Slides

## Slide 2: Agenda
1. Define use cases of interest for the DT
2. Agree initial and prioritization of use cases for the DT to work on
3. DT Work assignment and planning
4. AOB

## Slide 3: Initial Set of DT Questions
Single-domain/Single-layer Use Case(s)
Italo Busi
Daniel King

## Slide 4
S1
S2
S3
s36
S4
S6
S37
s38
S9
S10
S11
Network domain 1
S21
S22
S23
S25
S24
S26
S27
S28
S29
S30
S31
Network domain 2
C-R1
C-R2
C-R3
C-R4
C-R5
C-R6
Customer domain 1
Customer domain 2
Network domain 3
S39
Customer domain 3
C-R7
C-R8
ODUk link
Note:
OTN-Optical layer
controlled by each domain controller
and not exposed
Via Controller NBI.
Figure provided by Igor

## Slide 5: Controlling Hierarchy
MDSC
PNC1
PNC2
PNC3
Assumption:
1: client controller knows the C-Rx and its access link information.
2: MDSC knows how to map C-Rx and its network side of nodes within its network domain.
3: MDSC has no topology information at all before each PNC reports its topology.
Network Domain 1
Network domain 3
Network Domain 2
Client Controller
Notes: How does MDSC know #2?

## Slide 6: Controlling Hierarchy – single domain
MDSC
PNC1
Network Domain 1
Client Controller
CMI: connectivity between C-R1 and C-R2
MPI: connectivity between C-R1 and C-R2
Single-layer use cases can cover both cases where there is only one network domain/PNC as well as multi-domain use cases where the connectivity request at the CMI is between access links attached to the same network domain
Assumptions:
CMI is the same: customer is not aware of whether the network or connectivity request is single or multi domain
MPI is the same: PNC is not aware of the existence of other PNCs
Notes: How does MDSC know #2?

## Slide 7
S1
S2
S3
S4
S6
S9
S10
S11
Network domain 1
C-R1
C-R2
C-R3
Customer domain 1
ODUk link
Note:
OTN-Optical layer
controlled by each domain controller
and not exposed
Via Controller NBI.
Figure provided by Igor

## Slide 8: Comments/Questions
Single-domain assumption: only one PNC
Single-layer assumptions:
  All NEs are switching at the LO ODU level
    LO ODU multiplexing into HO ODU is not used or pre-configured (and not controlled at the MPI)
What type of topology abstraction? White, black or grey?
What about client layer services?
  ODU transit service
  Other (non ETH) OTN client services (e.g., STM-N, FC, InfiniBand, …): single-layer or multi-layer?
    Does white/grey topology apply here?
  EPL over ODU: single-layer or multi-layer?
    Does it depend from black, white or grey topology?
    Transparent versus frame-based mapping
  EVPL over ODU: single-layer or multi-layer?
    Does it depend from black, white or grey topology?
What about multi-function access link?

## Slide 9
S1
S2
S3
S4
S6
S9
S10
S11
Network domain 1
C-R1
C-R2
C-R3
Customer domain 1
STM-N/FC/IB/… link
Note:
OTN-Optical layer
controlled by each domain controller
and not exposed
Via Controller NBI.
Figure provided by Igor
Other OTN client services

## Slide 10
S1
S2
S3
S4
S6
S9
S10
S11
Network domain 1
C-R1
C-R2
C-R3
Customer domain 1
10GE link
Note:
OTN-Optical layer
controlled by each domain controller
and not exposed
Via Controller NBI.
Figure provided by Igor
EPL over ODU Services

## Slide 11
S1
S2
S3
S4
S6
S9
S10
S11
Network domain 1
C-R1
C-R2
C-R3
Customer domain 1
10GE link
Note:
OTN-Optical layer
controlled by each domain controller
and not exposed
Via Controller NBI.
Figure provided by Igor
EVPL over ODU Services

## Slide 12
S1
S2
S3
S4
S6
S9
S10
S11
Network domain 1
C-R1
C-R2
C-R3
Customer domain 1
Multi-function access link
Note:
OTN-Optical layer
controlled by each domain controller
and not exposed
Via Controller NBI.
Figure provided by Igor
Multi-function access link
When C-R3 is connected with C-R1:
C-R3 access link is configured as an STM-64 link
When C-R3 is connected with C-R2:
C-R3 access link is configured as a 10GE link