## Slide 1: Use Cases 1 Analysis
Single-domain/Single-layer Use Case(s)

## Slide 2: High-Level analysis

## Slide 3: Reference Network Scenario
S1
S2
S3
S4
S6
S9
S10
S11
Transport domain
C-R1
C-R2
C-R3
IP domain
C-R5
C-R4

## Slide 4: Controlling Hierarchy
MDSC
IP PNC
IP Network Domain
Client Controller
Transport PNC
Transport Network Domain
CMI (initially out of scope)
IP MPI
(out of scope)
Transport MPI
(in the scope)

## Slide 5: Abstract White Topology @MPI
ODU Abstract
Topology
@MPI
C-R1
C-R2
C-R3
C-R5
C-R4
S3-1
S6-2
S3
S6
S1
S2
S4
S5
S7
S8
PNC exports as abstract topology at MPI: TE nodes (since the white topology abstraction is used, they represents physical nodes) , TE links (between TE nodes) , access-links (facing transport border nodes) , transport border nodes and link termination points (LTPs) (e.g.S3-1 and S6-2)
The IP domain (reported here in the blue rectangle) is not part of the topology exported. They are included in this picture just to show the end points of the access links.
The topology model provides «external-domain» container that alows the MDSC to glue togather the different domains to create E2E abstract multi-domain topology.
S6-1

## Slide 6: ODU Transit (ODU2)
S1
S2
S3
S4
S5
S6
S7
S8
Transport domain
C-R1
C-R2
C-R3
C-R5
C-R4
ODUk link
Note: OTN-Optical layer controlled by each domain controller and not exposed Via Controller NBI.
Traffic flow from C-R1 to C-R3:
C-R1 (PKT -> ODU2), S3 (ODU2), S5 (ODU2), S6 (ODU2), C-R3 (ODU2 -> PKT)
Note - C-R1 (PKT -> ODU2) and C-R3 (ODU2 -> PKT) adaptations not controlled by Transport PNC
S3-1
S6-2

## Slide 7: ODU2 Tunnel Setup
Abstract
Topology
@MPI
C-R1
C-R2
C-R3
C-R5
C-R4
MDSC should request Transport PNC to setup an ODU2 Tunnel (Segment) between S3-1 and S6-2
Ingress and egress points are indicated in the explicit-route-objects of the primary path:
  First element of the explicit-route-objects refers to S3-1 LTP
  Last element of the explicit-route-objects refers to S6-2 LTP
  The tunnel to be setup is a segment tunnel, source and destination of the E2E tunnel
  information is belonging to customer side.
S3-1
S6-2
S3
S6
S1
S2
S4
S5
S7
S8

## Slide 8: ODU2 Path Computation
Abstract
Topology
@MPI
C-R1
C-R2
C-R3
C-R5
C-R4
MDSC should request Transport PNC path computation for an ODU2 Tunnel (Segment) between S3-1 and S6-2
In case of stateful path computation, a pre-computed ODU2 Tunnel is created with ingress and egress points indicated in the explicit-route-objects of the primary path (like in the previous slide)
In case of stateless path computation, TBD (how to request a path computation between S3-1 and S6-2 using path computation RPC is still an open issue)
  Note – in PCEP it is not possible to request the PCE to retun the set of available labels on the inter-domain links for each computed path
S3-1
S6-2
S3
S6
S1
S2
S4
S5
S7
S8

## Slide 9: Other OTN client services (STM-64)
S1
S2
S3
S4
S6
S9
S10
S11
Transport domain
C-R1
C-R2
C-R3
C-R5
C-R4
STM-N/FC/IB/… link
Traffic flow from C-R1 to C-R3:
C-R1 (PKT -> STM-64), S3 (STM-64 -> ODU2), S6 (ODU2), S9 (ODU2 -> STM-64), C-R3 (STM-64 -> PKT)
Note - C-R1 (PKT -> STM-64) and C-R3 (STM-64 -> PKT) adaptations not controlled by Transport PNC
ODU link

## Slide 10: EPL over ODU Services (10GE)
S1
S2
S3
S4
S6
S9
S10
S11
Transport domain
C-R1
C-R2
C-R3
C-R5
C-R4
10GE link
Traffic flow from C-R1 to C-R3:
C-R1 (PKT -> ETH), S3 (ETH -> ODU2), S6 (ODU2), S9 (ODU2 -> ETH), C-R3 (ETH-> PKT)
Note - C-R1 (PKT -> ETH) and C-R3 (ETH-> PKT) adaptations not controlled by Transport PNC
ODU link

## Slide 11: EVPL over ODU Services
S1
S2
S3
S4
S6
S9
S10
S11
Transport domain
C-R1
C-R2
C-R3
C-R5
C-R4
10GE link
Traffic flow from C-R1 to C-R3:
C-R1 (PKT -> VLAN), S3 (VLAN -> ODU0), S6 (ODU0), S9 (ODU0 -> VLAN), C-R3 (VLAN-> PKT)
Note - C-R1 (PKT -> VLAN ) and C-R3 (VLAN -> PKT) adaptations not controlled by Transport PNC
ODU link

## Slide 12: Multi-function access link
S1
S2
S3
S4
S6
S9
S10
S11
Transport domain
C-R1
C-R2
C-R3
C-R5
C-R4
Multi-function access link
10GE link
STM-64 link
ODUk link

## Slide 13: Multi-function access link
When C-R3 is connected with C-R1:
  C-R3-S9 access link is configured as a 10GE link
  Traffic flow from C-R1 to C-R3:
  C-R1 (PKT -> ETH), S3 (ETH -> ODU2), S6 (ODU2), S9 (ODU2 -> ETH), C-R3 (ETH -> PKT)
When C-R3 is connected with C-R4:
  C-R3-S9 access link is configured as an ODUk link
  Traffic flow from C-R4 to C-R3:
  C-R4 (PKT -> ODU2), S3 (ODU2), S6 (ODU2), S9 (ODU2), C-R3 (ODU2 -> PKT)
When C-R3 is connected with C-R5:
  C-R3-S9 access link is configured as a STM-64 link
  Traffic flow from C-R1 to C-R3:
  C-R5 (PKT -> STM-64), S3 (STM-64-> ODU2), S6 (ODU2), S9 (ODU2 -> STM-64), C-R3 (STM-64 -> PKT)
Note - C-R1 (PKT -> ETH), C-R4 (PKT -> ODU2), C-R5 (PKT -> STM-64), C-R3 (ETH -> PKT) , C-R3 (ODU2 -> PKT) and C-R3 (STM-64 -> PKT) adaptations not controlled by Transport PNC

## Slide 14: Detailed analysis

## Slide 15: ODU2 Tunnel Setup - Remind
Abstract
Topology
@MPI
C-R1
C-R2
C-R3
C-R5
C-R4
S3-1
S6-2
S3
S6
S1
S2
S4
S5
S7
S8
S3-2
S5-1
S5-2
S6-3

## Slide 16: ODU2 Connection: TEAS Tunnel Model Instantiation
ODU2 Connection
<te>
<tunnels>
<lsps-state>
<lsp>
src: 0.0.0.0
dest: 0.0.0.0
tunnel-id:1
lsp-id: ODU2-lsp-1-id
type: tunnel-p2p
lsp-oper-status: up
lsp-protection-role: working
<config>
name: ODU2-Service-1
identifier: 1
type: tunnel-p2p
bandwidth: 10Gbps
lsp-prot-type: unprotected
admin-status: state-up
<tunnel>
name: <ODU2-Service-1 ref>
identifier: <1>
<p2p-primary-paths>
<config>
type: explicit
<state>
type: explicit
<lsp>
<lsp-ref>
<lsp-record-route>
<explicit-route-objects>
index: 0
e-r-usage: route-include-ero
type: unnumbered-link
router-id: S3
interface-id: S-LTP-3
<rro>
subobject-index: 0
router-id: S3
interface-id: S-LTP-3
<te>
<tunnels>
<primary-paths>
Config Datastore
Operational/State Datastore
<explicit-route-objects>
index: 1
e-r-usage: route-include-ero
type: unnumbered-link
router-id: S6
Interface-id: S-LTP-6
<rro>
subobject-index: TBD
router-id: S6
Interface-id: S-LTP-6
TE Tunnel and Topology Models will provide some clarification about this mapping in the attribute description
The label to identify the spcecific ODU2 could be defined by an explicit-route object following the explicit-route objects identifying the access links
<state>
name: ODU2-Service-1
identifier: 1
type: tunnel-p2p
bandwidth: 10Gbps
lsp-prot-type: unprotected
admin-status: state-up
Oper-status
<tunnels>
Reverse direction
Waiting for feedbacks from TEAS WG about this assumption
<bidirectional>
<association>
type: bidir-assoc-corouted
Assumption:
- The attributes id, source and global-source are not specified (required) for bidirectional co-routed Tunnels
- The provisioing attribute is not needed at the MPI
<bidirectional>
<association>
type: bidir-assoc-corouted

## Slide 17: Open Issues

## Slide 18
How MDSC knows which TS are available at access link?
-> Provided by Transport PNC and IP PNC (via Topology model)
Action – check with TE Topology DT whether this information is available or not in the base TE Topology model or should be provided in the ODU Topology augmentation. We can also prepare a proposal to update the YANG model.
2) How MDSC selects the TS to be used on the access link
-> Based on available TSs, its own TS allocation policy and administrative configuration
-> suggested PNC?
3) How MDSC configures the TS to be sued on the access link
-> Using the Tunnel model (ERO)
MDSC creates a Tunnel in the Transport MPI YANG data store (POST). In this step MDSC configures the TSs on the access links.
PNC performs some initial checks and, if the request is ok, confirms to MDSC the successful creation of the Tunnel in the YANG data store (HTTP 200 - Success)
PNC setup the ODU tunnel in the transport network data plane
PNC updates the Tunnel state in the YANG data store
MDSC is notified of the Tunnel state change in the YANG data store
MDSC creates a Tunnel in the Transport MPI YANG data store (POST). In this step MDSC configures the TSs on the access links.
PNC performs some initial checks and, if the request is ok, confirms to MDSC the successful creation of the Tunnel in the YANG data store (HTTP 200 - Success)
PNC fails to setup the ODU tunnel in the transport network data plane (e.g., because of available resources)
How PNC informs MDSC that the tunnel cannot be setup in the network? We may need some Tunnel state to indicate whether tunnel setup is in-progress, failed or success. Do we have this status in TE Tunnel model? Could we use a timeout? To be investigated by the DT

## Slide 19
BASIC question
Who configure label/TS on access link?
Is the MDSC that has to be the master of operation?
How the PNCs provide labels/TS to MDSC?

## Slide 20: Comments/Questions
Single-domain assumption: only one PNC
Single-layer assumptions:
  All NEs are switching at the LO ODU level
    LO ODU multiplexing into HO ODU is not used or pre-configured (and not controlled at the MPI)
What type of topology abstraction? White, black or grey?
  Start assuming a white topology abstraction
  We can think later if we need also to analyze black or grey topology abstractions
What about client layer services?
  ODU transit service
  Other (non ETH) OTN client services (e.g., STM-N, FC, InfiniBand, …): single-layer or multi-layer?
  EPL over ODU: single-layer or multi-layer?
    Transparent versus frame-based mapping?
  EVPL over ODU: single-layer or multi-layer?
  Assumption: single-layer (no multiplexing/switching)
What about multi-function access link?
  To be addressed
  Assumption: single-layer (no multiplexing/switching)

## Slide 21
In this scenario the tunnel is not terminate in the OTN NW, it is a «Transit tunnel» , starting from router side
How can we get information regarding the ingress and egrees point of the transit tunnel (router-id and interface-id) ?
  The router id can be the te-node-id in the teas-topology
  The interface-id can be the te-tp-id in the teas-topology
The same problem appear for lsp-state part with RRO
Action (Sergio) – Check with TE Tunnel model experts for clarification
How the specific ODU2 (e.g., TS information) to be used on the access links is configured
  Some negotiation process is needed
  It may depend on how this information is selected:
    If selected by the NE/PNC, it is communicated by the PNC to the MDSC after the Tunnel has been setup
    If selected by others (e.g., MDSC), it should be communicated by the MDSC in the ERO elements when the Tunnel setup is requested
  Current assumption: the MDSC selects the specific ODU2
If MDSC selects the ODU2 to be used on the access link it is not clear how it could get the information about the available TSs among which it can select
  Possible conclusion: it is beneficial not to advertise the available BW in terms of number of containers but we advertise which particular container is available. This information may be needed only for Tunnel configuration while for path computation this information is not needed.
Action (DT) – Continue to investigate this open issue