## Slide 1: Transport NBI Design Team Update
Italo Busi
Daniel King

## Slide 2: Transport NBI DT
IETF is developing a set of YANG Models that could be used for Transport NBI
  How existing IETF YANG Models can be used for transport networks?
  Are there any gaps in the existing IETF YANG Models?
TNBI DT is currently looking at
  Use Cases
  Analysis of how existing IETF YANG models can be used to support these Use Cases
Working method
  Mailing list
  Weekly conference calls on Wednesday at 3:00pm CET
  GitHub: https://github.com/danielkinguk/transport-nbi

## Slide 3: Use Cases
Use Case I-D published:
  https://tools.ietf.org/html/draft-tnbidt-ccamp-transport-nbi-use-cases-01
Currently covers
  Use Case 1: Single-domain with single-layer
    Reference Network
    Controlling Hierarchy
    Topology Abstraction
    Service Description of ODU transit, EPL and other OTN Client Services
Next steps
  Complete Use Case 1
    Service Description of of EVPL, EVPLan, EVPTree and Virtual Network Services
    Considerations about multi-service access links
  Use Case 2: Single-domain with multi-layer
  Use Case 3: Multi-domain with single-layer
  Use Case 4: Multi-domain and multi-layer

## Slide 4: Analysis
Analysis started – no I-D submitted yet
  Use Case 1 for ODU Transit Service analyzed
  Some comments/questions already discussed with TE-Tunnel model authors
Next Steps
  Address pending open issues
  Complete analysis of Use Case 1
  Analysis of other Use Cases

## Slide 5: Use Case 1
S1
S2
S3
S4
S6
S9
S10
S11
Transport domain
C-R1
C-R2
C-R3
IP domain
C-R5
C-R4
MDSC
IP PNC
Client Controller
Transport PNC
CMI (initially out of scope)
IP MPI
(out of scope)
Transport MPI
(in the scope)

## Slide 6: ODU2 Tunnel Setup
Abstract
Topology
@MPI
C-R1
C-R2
C-R3
C-R5
C-R4
MDSC should request Transport PNC to setup an ODU2 Tunnel (Segment) between S-LTP-3 and S-LTP-6
Ingress and egress points are indicated in the ERO of the primary path:
  First ERO element is S-LTP-3
  Last ERO element is S-LTP-6
  The tunnel to be setup is a segment tunnel, source and destination of the E2E tunnel
  information is belonging to customer side.
S-LTP-3
S-LTP-6
S3
S6
S1
S2
S4
S5
S7
S8

## Slide 7: ODU2 Connection: TEAS Tunnel Model Instantiation
ODU2 Connection
<te>
<tunnels>
<lsps-state>
<lsp>
src: 0.0.0.0
dest: 0.0.0.0
tunnel-id:1
lsp-id: ODU2-lsp-1-id
type: tunnel-p2p
lsp-oper-status: up
lsp-protection-role: working
<config>
name: ODU2-Service-1
identifier: 1
type: tunnel-p2p
bandwidth: 10Gbps
lsp-prot-type: unprotected
admin-status: state-up
<tunnel>
name: <ODU2-Service-1 ref>
identifier: <1>
<p2p-primary-paths>
<config>
type: explicit
<state>
type: explicit
<lsp>
<lsp-ref>
<lsp-record-route>
<explicit-route-objects>
index: 0
e-r-usage: route-include-ero
type: unnumbered-link
S3
-LTP 3 ??
<rro>
subobject-index: 0
Router-id: ??
Interface-id: ??
<te>
<tunnels>
<primary-paths>
Config Datastore
Operational/State Datastore
<explicit-route-objects>
index: 1
e-r-usage: route-include-ero
type: unnumbered-link
S6
S-LTP-6
<rro>
subobject-index: 0
Router-id: ??
Interface-id: ??
1) Not clear how to get information about the router-id and interface-id from the TE topology
2) Not clear how to use the label to identify the spcecific ODU2
<config>
name: ODU2-Service-1
identifier: 1
type: tunnel-p2p
bandwidth: 10Gbps
lsp-prot-type: unprotected
admin-status: state-up
Oper-status
<tunnels>
Reverse direction
Could we use the explicit-route-usage attribute to identify the ERO representing the incoming and outgoing ports from the domain?

## Slide 8: Open Issues
How can we get information regarding the ingress and egrees point of the transit tunnel (router-id and interface-id) ?
  The router id can be the te-node-id in the teas-topology?
  The interface-id can be the te-tp-id in the teas-topology?
How the specific ODU2 (e.g., TS information) to be used on the access links is configured
  Some negotiation process is needed
  It may depend on how this information is selected:
    If selected by the NE/PNC, it is communicated by the PNC to the MDSC after the Tunnel has been setup
    If selected by others (e.g., MDSC), it should be communicated by the MDSC in the ERO elements when the Tunnel setup is requested
  Current assumption: the MDSC selects the specific ODU2
How MDSC knows which TSs are available on the access link
  Possible conclusion: it is beneficial not to advertise the available BW in terms of number of containers but we advertise which particular container is available. This information may be needed only for Tunnel configuration while for path computation this information is not needed.
  Is this information provided by the TE-Topology or should be provided in the ODU augmentation?

## Slide 9: Open Issues (2)
Can PNC suggest label(s) to MDSC?
  May depend on the RESTconf operation sequence
RESTconf operation sequence
  Do we need to know if the Tunnel setup is in-progress, failed or success?
  Is this information available in the TE-Tunnel model?
  Could we use a timeout?
Should we also consider the YANG Transport Service Model (draft-zhang-ccamp-transport-ctrlnorth-yang)? Is it applicable only at the CMI or also at the MPI?
Which tool to use to describe the analysis? PowerPoint Instagram’s or textual description?

## Slide 10: Open Issues – Scope related (3)
Should we analyze only the IETF YANG models or at YANG models also from other SDOs (e.g., ONF, MEF, ...)
  Consider use cases for different SDOs
  Analyze applicability only of IETF YANG model
  Other SDOs can analyze applicability of their YANG models to the use cases
Where to document the analysis (same draft as Use Cases or different draft)?
  Describe the analysis in a different draft(s)
What about technology-specific augmentation of TE Tunnel model?
  An individual I-D already exists in CCAMP for the OTN tunnel model augmentation