## Slide 1: Recap of the unofficial gap analysis group work
Presenter: Sergio Belotti
Draft: https://tools.ietf.org/html/draft-zhang-ccamp-transport-yang-gap-analysis-01
Github: https://github.com/TransportModels/IETF-Transport-Modeling

## Slide 2: Contributors
Some main participants:
Michael Scharf (Nokia)
Anurag Sharma (Infinera)
Karthik Sethuraman (NEC)
Xian Zhang (Huawei)
Sergio Belotti (Nokia)
Oscar Gonzalez de Dios (Telefonica)
Tara Cummings (Ericsson)
Hans Bjursröm (Infinera)
Italo Busi (Huawei)

## Slide 3: Objective and Overview
Objective of this slides: to introduce the analyzed use cases, where the group are, what are the open issues and possible next steps.
Overview of discussed use cases:
  Use Case 1: Single Topology (one domain one layer);
  Use Case 2:Multilayer/single domain Topology;
  Use Case 3:Single layer/multi-domain Topology;
Note: slides with much more details can be downloaded from the github.

## Slide 4: Use Case - 1
Point-to-Point Service, Single Provider, Single Network Topology

## Slide 5: Mapping from Service/EVC to NRM Connections Different Providers
EVC (the end-to-end CarrierEthernetService)
OVC
OVC
ConnectivityService/OVC
ConnectivityService/OVC
UNI
Link
E-NNI
E-NNI
SP-UNI
Op-UNI
UNI
SP-UNI
Op-UNI
Connection
Connection
Link either not visible or “external”
managed object classes at Service level (potentially appearing at Legato, Interlude Management IRPs)
managed object classes at Resource level (potentially appearing at Presto for provisioning purposes)
managed object classes at Resource level (potentially appearing at Presto for discovery purposes, e.g. topology)
single Context for now
ConnectivityServicePort
ServiceEndPoint
ConnectionEndPoint
NodeEdgePoint
ConnectivityServicePort
ServiceEndPoint
ConnectionEndPoint
NodeEdgePoint
ConnectivityServicePort
ServiceEndPoint
ConnectionEndPoint
NodeEdgePoint
ConnectivityServicePort
ServiceEndPoint
ConnectionEndPoint
NodeEdgePoint
Node
Node
Notes: MEF 26.2
It is also possible that a single OVC in an Operator CEN can support more than one EVC. This can occur when an OVC End Point Map Service Attribute value has Bundling.
It is important to note that the Operator UNI Service Attributes are different from the UNI Service Attributes detailed in MEF 10.3. They are different because the value of each Operator UNI Service Attribute is agreed to by the SP/SO and the Operator while the value of each UNI Service Attribute described MEF 10.3 is agreed to by the Subscriber and the Service Provider.

## Slide 6: Point-to-Point Service, Single Provider, Single Network Topology
NE-B
NE-A
Network = “Network-A”
UNI/LTP
(TP-U-A)
ForwardingDomain
OTU4
(TP-U-OTU4-A)
ODU4 (HO)
(TP-U-ODU4-A)
ODU2 (LO)
(TP-U-ODU2-A-1)
UNI/LTP
(TP-U-B)
OTU4
(TP-U-OTU4-B)
ODU4 (HO)
(TP-U-ODU4-B)
ODU2 (LO)
(TP-U-ODU2-B-1)
Line Side/LTP
(TP-L-A)
OTU4
(TP-L-OTU4-A)
ODU4 (HO)
(TP-L-ODU4-A)
ODU2 (LO)
(TP-L-ODU2-A-1)
Line Side/LTP
(TP-L-B)
OTU4
(TP-L-OTU4-B)
ODU4 (HO)
(TP-L-ODU4-B)
ODU2 (LO)
(TP-L-ODU2-B-1)
Access Link
Service-1
LID-FWD-1 (Link ID)
LID-REV-1
TE Link
GbE 0/1
GbE 0/1
R1
(10.0.0.100)
R2
(10.0.0.101)
Comments (06/21/16): Remove OTU4. Split ODU4 into ODU4 Edge Point and ODU4. Links associated with ODU4 edge points.

## Slide 7: Network Topology (i2rs) Model Instantiation
<networks>
<network>
network-id=Network-A
<networks-state>
<network>
network-ref: <NW-A ref>
server-provided: true
<link>
link-id: LID-FWD-1
<source>
src-node: <NE-A ref>
source-tp: <TP-L-A ref>
<destination>
dest-node: <NE-B ref>
dest-tp: <LTP-L-B ref>
<link>
link-id: LID-REV-1
<source>
src-node: <NE-B ref>
source-tp: <LTP-L-B ref>
<destination>
dest-node: <NE-A ref>
dest-tp: <TP-L-A ref>
<node>
node-id: NE-A
<node>
node-id: NE-B
<network-types>
<termination-point>
tp-id: TP-UNI-A
<termination-point>
tp-id: TP-U-OTU4-A
<termination-point>
tp-id: TP-U-ODU4-A
<termination-point>
tp-id: TP-L-A
<termination-point>
tp-id: TP-L-OTU4-A
<termination-point>
tp-id: TP-L-ODU4-A
<supporting-t…-p...>
network-ref: <NW-A ref>
node-ref: <NE-A ref>
tp-ref: <TP-UNI-A ref>
<supporting-t…-p…>
network-ref: <NW-A ref>
node-ref: <NE-A ref>
tp-ref: <TP-U-OTU4-A ref>
<supporting-t…-p…>
network-ref: <NW-A ref>
node-ref: <NE-A ref>
tp-ref: <TP-L-A ref>
<supporting-t…-p…>
network-ref: <NW-A ref>
node-ref: <NE-A ref>
tp-ref: <TP-L-OTU4-A ref>
UNI side TPs
Same structure as NE-A
Missing Transport Topology & OTN Topology Type
Changing to
a module
NE Type & Version missing
<termination-point>
tp-id: TP-U-ODU2-A-1
<supporting-t…-p…>
network-ref: <NW-A ref>
node-ref: <NE-A ref>
tp-ref: <TP-U-ODU4-A ref>
<termination-point>
tp-id: TP-L-ODU2-A-1
<supporting-t…-p…>
network-ref: <NW-A ref>
node-ref: <NE-A ref>
tp-ref: <TP-L-ODU4-A ref>
Line side TPs
Missing
Generic attrs: TP type, oper status, rate, TP location (client, line, logical, etc.)
OTN attrs: TPN, timeslots, TSG
Comments (06/21/16):
OTN Topology type defined in L1Topology.
NE Type and Version should be optional. Cleaner solution is to have NE capability, e.g. ODU hierarchy, Mux levels, etc. in a OTN TE Topology model.
Generic attributes (similar to LayerProtocol) should be added to the augmented Transport Model.
Notes: 1. What should be Node Id: NE Id, IP Address? Something that does not change.

## Slide 8: TEAS Tunnel Model Instantiation
<te>
<tunnels>
<lsps-state>
<lsp>
src: 0.0.0.0
dest: 0.0.0.0
tunnel-id:tunnel-1-id
lsp-id: lsp-1-id
type: P2P
lsp-oper-status: up
lsp-protection-role: working
<config>
name: Service-1
tunnel-id: tunnel-1-id
type: p2p
bandwidth: 10Gbps
lsp-prot-type: unprotected
admin-status: up
<endpoint>
type: root
endpoint-address:0.0.0.0
network-id: <Network-A ref>
node-id: <NE-A ref>
tp-id: <TP-UNI-A ref>
<tunnel>
name: <Service-1 ref>
type: <p2p ref>
tunnel-id: <tunnel-1-id ref>
<endpoint>
type: root
endpoint-address:0.0.0.0
network-id: <Network-A ref>
node-id: <NE-B ref>
tp-id: <TP-UNI-B ref>
<primary-paths>
<config>
type: explicit
<state>
type: explicit
<lsp>
<lsp-ref>
<lsp-record-route>
<explicit-route-objects>
index: 0
e-r-usage: route-include-ero
type: link
link-ref: <LID-FWD-1 ref>
<rro>
subobject-index: 0
type: tp-ref
tp-ref: <TP-U-ODU2-A-1 ref>
<userlabel>
userlabel=NYC-LA-1
<userlabel>
userlabel=myservice-123
<te>
<tunnels>
<tunnel>
name: <Service-1 ref>
type: <p2p ref>
tunnel-id: <tunnel-1-id ref>
<state>
name: Service-1
tunnel-id: tunnel-1-id
type: p2p
bandwidth: 10Gbps
lsp-prot-type: unprotected
tunnel-oper-status: up
<endpoint>
type: root
endpoint-address:0.0.0.0
network-id: <Network-A ref>
node-id: <NE-A ref>
tp-id: <TP-UNI-A ref>
<endpoint>
type: root
endpoint-address:0.0.0.0
network-id: <Network-A ref>
node-id: <NE-B ref>
tp-id: <TP-UNI-B ref>
<primary-paths>
Config Datastore
Operational/State Datastore
<rro>
subobject-index: 1
type: link-ref
link-ref: <LID-FWD-1 ref>
<rro>
subobject-index: 2
type: tp-ref
tp-ref: <TP-U-ODU2-A-1 ref>
Notes: Refs not used for tunnel ids. That is, tunnel id value is duplicated at multiple places like lsp.
What is the purpose of having ERO under the primary path state?

## Slide 9: Use Case - 2
E2E Service in ML Topology

## Slide 10: E2E Service in ML Topology
Source: T-API FRS
PE1-1
PE2-1
PE1-1.1
PE2-1.1
PE1-1.2
PE2-1.2
ETHNetwork B
OTNNetwork A
ETH-UNI
TTP 2
TTP 4
Tun-id-1-fw

## Slide 11: TL implications
ETH link in red dashed line does not exist until OTN server trail (ODU2 connection) is created.
From topology prospective TL exist to indicate “potential” layer transition and connectivity
When server trail is created , ETH network will add the ETH link in the ETH topology
ETH link is supported by the OTN tunnel (ODU2 connection)
Until TL is not used, does not exists any I2RS Link related .
As soon as ODU2 tunnel is created (with teas-yang-te draft), ETH link is appearing in the ETH topology.
TL permits multi-layer topology representation for path computation, so should belongs to 1 topology.

## Slide 12: Multi-layer node decomposition Example: L1+L0 OTN switch
TP1
N2
TPn
● ● ●
TP21
TP2n
● ● ●
Logical sub-node N2_L1
OCh TP
Logical sub-node N2_L0
ODUk TPs
Dual-layer node N2 is decomposed into 2 logical sub-nodes: N2_L1 and N2_L0
Transitional link between N2_L1 and N2_L0 with following TPs on the link ends: N2_L1 side: set of ODUk TPs, N2_L0 side: OCh TP  server trail TP
Example: 100G OCh TP  ODUk TPs {80 x ODU0, 40 x ODU1, 10 x ODU2, 2 x ODU3, 1 x ODU4}
transitional link with client/server
adapt./term.
Layer 1
Layer 0
Transformation: physical view to topological view
Potential ODUk connections
Potential server trails
Note:only one OCH trail is represented. This trail can support “many”ODUk connections of which ODUk TPs are the connection points of the potential ODUk connections supported

## Slide 13: Transitional Link
draft-ietf-teas-yang-te-topo-05
Tunnel Termination Point (TTP)
Server Link Termination Point (S-LTP)
Client Link Termination Point (C-LTP)
TTP-1
TTP-2
LTP-6
LTP-1
LTP-5
LTP-4
LTP-3
LTP-2
TTP-3
C-LTP-1,2,3
C-LTP-4,5,6
TTP-1
TTP-2
LTP-6
LTP-1
LTP-5
LTP-4
LTP-3
LTP-2
TTP-3
C-LTP-1,2,3
C-LTP-4,5,6
Transformation
Logical Sub-node
Transitional Link
TTP client
Layer 2
Layer 3
Layer 1

## Slide 14: Logical nodes separation
Link 1-2
LTP
TTP
PE1
PE1-E
PE1-O
Link
Transitional Link
Connection
PE1-1.1
PE1-1.2
ODU2
PE1.2
PE1.3
PE1.1
TTP-1
TTP-2

## Slide 15: Added Support for Multi-layer Topology
draft-ietf-teas-yang-te-topo-05
augment /nw:networks/nw:network/nw:node:
+--rw te!
+--rw tunnel-termination-point* [tunnel-tp-id]
+--rw tunnel-tp-id binary
+--rw config
| +--rw switching-capability? identityref
| +--rw encoding? identityref
+--ro state
+--ro switching-capability? identityref
+--ro encoding? identityref
augment /nw:networks/nw:network/nt:link:
+--rw te!
+--rw config
| +--rw te-link-attributes
| +--rw interface-switching-capability* [switching-capability]
| | +--rw switching-capability identityref
| | +--rw encoding? identityref
| | +--rw max-lsp-bandwidth* [priority]
+--ro state
+--ro is-transitional? empty
Transitional link
  Connects link termination points at different layers.
Modeling abstraction
  Added switch-layer attributes to TE Link Termination Point.
  Added a flag to TE Link to indicate transitional.
“Layer 1” at one end, “Layer 2” at other end.
Which is the client and which the server with this coding ?
What about adding “sub-node” concept at this point, related to specific TTP?

## Slide 16: TL Questions
Hom many nodes have to be existing in the topology?
  1 logical ETH node + 1 logical OTN node
    ETH topology + OTN topology
    ETH link in red dashed line does not exist until OTN server trail (ODU2 connection) is created.
  1 node (two sub-logical node) but the node is part of 1 topology (ETH) and OTN node is “supporting” node ?
At I2RS level the TL link should be the link between two TTP. But TTP is visible at topology level or just in te-topology for path computation purpose?
  TTP is described in the te-node augmentation, not as augmentation from i2rs TP.

## Slide 17: ETH Topology (i2rs) Model Instantiation
<networks>
<network>
network-id=Network-B
<link>
link-id: LID-NWB-FWD-1
<source>
src-node: <PE1-1 ref>
source-tp: <PE1-1.2 ref>
<destination>
dest-node: <PE2-1 ref>
dest-tp: <PE2-1.2 ref>
<link>
link-id: LID-NWB-REV-1
<source>
src-node: <PE2-1 ref>
source-tp: <PE2-1.2 ref>
<destination>
dest-node: <PE1-1 ref>
dest-tp: <PE1-1.2 ref>
<node>
node-id: PE1-1
<node>
node-id: PE2-1
<network-types>
[ETH]
<termination-point>
tp-id: PE1-1.1
<termination-point>
tp-id: PE1-1.2
<termination-point>
tp-id: PE2-1.1
<termination-point>
tp-id: PE2-1.2
ETH Link
[PE1-1.2 <-> P2-1.2]
This “link” does not exist in the i2rs until TL is not used.

## Slide 18: OTN Topology (i2rs) Model Instantiation
<networks>
<network>
network-id=Network-A
<link>
link-id: LID-NWA-FWD-1
<source>
src-node: <PE1 ref>
source-tp: <PE1.2 ref>
<destination>
dest-node: <P ref>
dest-tp: <P.1 ref>
<link>
link-id: LID-NWA-REV-1
<source>
src-node: <P ref>
source-tp: <P.1 ref>
<destination>
dest-node: <PE1 ref>
dest-tp: <PE1.2 ref>
<node>
node-id: PE1
<node>
node-id: PE2
<network-types>
[OTN]
<termination-point>
tp-id: PE1.1
<termination-point>
tp-id: PE1.2
<termination-point>
tp-id: PE1.3
<termination-point>
tp-id: PE2.1
<termination-point>
tp-id: PE2.2
<termination-point>
tp-id: PE2.3
<node>
node-id: PE3
<node>
node-id: P
<termination-point>
tp-id: PE3.1
<termination-point>
tp-id: PE3.2
<termination-point>
tp-id: PE3.3
<termination-point>
tp-id: P.1
<termination-point>
tp-id: P.2
<termination-point>
tp-id: P.3
<termination-point>
tp-id: PE3.4
<termination-point>
tp-id: P.4
OTN Link-1
[PE1.2 <-> P.1]
OTN Link-2
[P.2 <-> PE2.1]
OTN Link-3
[P.4 <-> PE3.2]
OTN Link-4
[PE1.3 <-> PE3.1]
OTN Link-5
[PE2.3 <-> PE3.3]

## Slide 19: ODU2 Connection: TEAS Tunnel Model Instantiation
ODU2 Connection
<te>
<tunnels>
<lsps-state>
<lsp>
src: 0.0.0.0
dest: 0.0.0.0
tunnel-id:ODU2-tunnel-1-id
lsp-id: ODU2-lsp-1-id
type: P2P
lsp-oper-status: up
lsp-protection-role: working
<config>
name: ODU2-Service-1
tunnel-id: ODU2-tunnel-1-id
type: p2p
bandwidth: 10Gbps
lsp-prot-type: unprotected
admin-status: up
Source:PE1 ip adr
Destination:PE2 ip adr
Src-tp-id: PE1.1 id/TTP2 in PE1
Dst-tp-id: PE2.2/TTP4 in PE2
<Hierarchical-link-id>
Local-te-node-id=PE1-1
Local-te-link-tp-id=PE1-1.2
Remote-te-node-id=PE2-1
Te-topology-id=Network-B
<tunnel>
name: <ODU2-Service-1 ref>
type: <p2p ref>
tunnel-id: <ODU2-tunnel-1-id ref>
<primary-paths>
<config>
type: explicit
<state>
type: explicit
<lsp>
<lsp-ref>
<lsp-record-route>
<explicit-route-objects>
index: 0
e-r-usage: route-include-ero
type: link
link-ref: < tun-id-1-fw>
<rro>
subobject-index: 0
type: link-ref
link-ref: <LID-NWA-FWD-4
ref>
<te>
<tunnels>
<tunnel>
name: <ODU2-Service-1 ref>
type: <p2p ref>
tunnel-id: <tODU2-unnel-1-id ref>
<state>
name: ODU2-Service-1
tunnel-id: ODU2-tunnel-1-id
type: p2p
bandwidth: 10Gbps
lsp-prot-type: unprotected
tunnel-oper-status: up
<primary-paths>
Config Datastore
Operational/State Datastore
<explicit-route-objects>
index: 1
e-r-usage: route-include-ero
type: link
link-ref: <tun-id-1-rev
ref>
<rro>
subobject-index: 0
type: link-ref
link-ref: <LID-NWA-FWD-4
ref>
LO ODU Src & Dest not shown
Do we need to put here TTP or related LTP?
It would be ETH link supported by OTN tunnel

## Slide 20: TEAS Topology Model: Dynamic ETH link Instantiation
<networks>
<network>
network-id=Network-A, provider-id= x client-id= ..
<networks-state>
<network>
network-ref: <NW-A ref>
server-provided: true
<node>
node-id: PE1-1
<termination-point>
tp-id: PE1-1.1
<termination-point>
tp-id: …
<termination-point>
tp-id: ….
<network-types>
=/te-topology/eth-topology
< underlay-topology >
Provider-id: <Y>
Network-id: <….>
Client-id: <0>
<termination-point>
tp-id:PE1-1.2
<link>
Link-id: ETH-1
<link>
Link-id: Linkx
<source>
src-node: <PE1-1>
source-tp: <PE1-1.2>
<destination>
dest-node: <PE2-1>
dest-tp: <PE2-1.2>
< connectivity matrix>
The capability between each TP pairs
<link attributes>
I2rs-yang-network-topo
Underlay: true
Provider-id=Y
<Underlay-tunnel-src>
tp-ref=PE1.1
Node-ref=PE1
Underlay-tunnel-dst>
Tp-ref=PE2.2
Node-ref=PE2
<config>
<node>
node-id: PE2-1
Do we need to put here TTP or related LTP?

## Slide 21: Transitional Link: TEAS Topology Model :multi-layer representation
<network>
network-id=Network-B
<link>
link-id: <Link1-2>
<te>
<state>
is-transitional
oper-status: up
information-source: system-processed
<config>
Config tree not shown
<source>
src-node: <PE1 –E ref>
source-tp: <TTP-1 ref>
Are TTP visible into I2rs topology?
<dest>
dst-node: <PE1 –O ref>
dst-tp: <TTP-2 ref>
To be completed

## Slide 22: Modeling of TL
Using Plug Ids: Separate topology instance is modeled for each technology layer. Transitional Links are first class link entities (Link defined in i2rs model) between Link-TPs present in two topologies. Since links are uni-directional, two links are present between Link-TPs, one for each direction. For each link the link source is set while the link destination is empty. Both links will have the same unique plug-id, which can be set by the NB provider, or the domain controller. Controller/Orchestrator will stitch two topologies together using the plug id modeled on the TL.
Single topology: Model multi-layer topologies as a single topology. In this case, both TLs are contained under the parent topology. The modeling of TL is simpler with this option, however there are multiple downsides with this option. Firstly, collapsing multiple layer topology into a single topology makes this topology very complex. It makes it more difficult for orchestrator to retrieve and control a single topology, when required. Secondly, single topology will require multiple augmentations, one for each technology layer that is collapsed.

## Slide 23: Use Case - 3
Multi-domain case

## Slide 24
S1
S2
S3
s36
S4
S6
S37
s38
S9
S10
S11
Network domain 1
S21
S22
S23
S25
S24
S26
S27
S28
S29
S30
S31
Network domain 2
C-R1
C-R2
C-R3
C-R4
C-R5
C-R6
Customer domain 1
Customer domain 2
Network domain 3
S39
Customer domain 3
C-R7
C-R8
ODUk link
Note:
OTN-Optical layer
controlled by each domain controller
and not exposed
Via Controller NBI.
Figure provided by Igor

## Slide 25: Controlling Hierarchy
MDSC
PNC1
PNC2
PNC3
Assumption:
1: client controller knows the C-Rx and its access link information.
2: MDSC knows how to map C-Rx and its network side of nodes within its network domain.
3: MDSC has no topology information at all before each PNC reports its topology.
Network Domain 1
Network domain 3
Network Domain 2
Client Controller
Notes: How does MDSC know #2?

## Slide 26: Domain controller reporting
MDSC
PNC1
PNC2
PNC3
Domain 1 abstract TE topologies (single node)
Domain 2 abstract TE topologies
Domain 3 abstract TE topologies
NE-A
PNC1 (single node)
PNC3 (same as physical topology)
PNC2 (single node)
NE-B
NE-C
NE-A
NE-D
NE-1
Notes: Confusing with repetition of NE-A, and node names for PNC3 do not match to those in slide 3.

## Slide 27: Network Topology (teas + i2rs) Model Instantiation (PNC1 to MDSC)
<networks>
<network>
network-id=Network-A, provider-id= provider PNC1, client-id= MDSC
<networks-state>
<network>
network-ref: <NW-A ref>
server-provided: true
<node>
node-id: NE-A
<termination-point>
tp-id: TP-1
<termination-point>
tp-id: …
All UNI/NNI side TPs
Changing to
a module
<termination-point>
tp-id: TP-7
<network-types>
=/te-topology/otn-topology
< underlay-topology >
Provider-id: <…>
Network-id: <….>
Client-id: <0>
<termination-point>
tp-id: …
<link>
Link-id: Link1
<link>
Link-id: Link7
<source>
src-node: <NE-A ref>
source-tp: <TP-1 ref>
<destination>
dest-node: <NULL>
dest-tp: <NULL>
< connectivity matrix>
The capability between each TP pairs
<external-domain>
Remote-te-node-id: <…>
Remote-te-link-tp-id: <…>
Plug-id: : <1>
<link attributes>
Total bandwidth: <100G>
Available bandwidth: NOT USED
Available ODU list: <40*ODU1, 10*ODU2, etc.>
Note:
1: PNC2 will report something similar;
2: PNC3 will report as described in use case 1(additional
intra-domain links/attributes;
I2rs-yang-network-topo
If nothing is provided, it can either be:
No constraints at all;
Path computation request (draft-busibel-teas-yang-path-computation)

## Slide 28: What does MDSC get?
Domain 2 abstract TE topologies
NE-3
NE-5
NE-2
NE-4
NE-6
NE-1
C-R1
C-R2
C-R3
C-R4
C-R5
C-R6
C-R7
C-R8
MDCS merges what is gets from PNCs and generate its own view of the multi-domain topology
Note:
1) Plug-id is needed to correctly connect inter-domain nodes;
2) What if the two link capabilities are not the same?
(see next page)
Notes: The interdomain links might be provisioned top down, rather that bottom-up discovery.
What are domain controllers sending?
How does MDSC stitch different domain controller topologies?
Different ways MDSC can persist and expose network?

## Slide 29: Non-identical Link attributes
Issue: what to do when the two links reported by different PNCs do not have identical attributes?
Solution: MDSC can keep what is mutual on both links in its own TED. In this case, only setting up ODU2 or ODU4 LSP/tunnel.
Domain 1 abstract TE topologies (single node)
Domain 2 abstract TE topologies
NE-A
PNC1 (single node)
PNC2 (single node)
NE-1
Plug-id=1
Plug-id=1
Total: 100G
80*ODU0;
10*ODU2;
1*ODU4;
Total: 100G
40*ODU1;
10*ODU2;
1*ODU4;
Notes: - MDSC should have the correct info and should fix the info in PNC.

## Slide 30: Open Issues and Possible Next-step
Open issues:
  To revisit some of the use cases if necessary;
    Bigger network size;
    More typical scenario;
    Etc;
  To identify any missing use cases and analyze further;
  ;
Possible Next-step:
  To follow up on some of the existing issues:
    Comments sent to TE YANG authors;
    How to provide path computation function;
    How to provide technology-specific tunnel models;
    Notification etc.
  To provide example code using some of the key YANG models;

## Slide 31
BACKUP

## Slide 32: MDSC – Path Computation
Domain 2 abstract TE topologies
NE-3
NE-5
NE-2
NE-4
NE-6
NE-1
C-R1
C-R2
C-R3
C-R4
C-R5
C-R6
C-R7
C-R8
Step 2: MDSC figures out the route based on its topology and it is shown in the figure.
Step 1: Client Controller sends a service request asking for a unprotected ODU tunnel/service from C-R2 to C-R6.

## Slide 33: MDSC=>PNC
MDSC
PNC1
PNC3
PNC2
Domain 1 abstract TE topologies (single node)
Domain 2 abstract TE topologies
NE-A
PNC1 (single node)
PNC2 (single node)
NE-1
Link2/tp2
Link4/tp4
Notes: Show connectivity matrix inside the NE.
Individual request coming down using the TE Tunnel model.

## Slide 34: TEAS Tunnel Model Instantiation (client => MDSC)
<te>
<tunnels>
<config>
name: Service-1
tunnel-id: tunnel-1-id
type: p2p
bandwidth: 10Gbps
lsp-prot-type: unprotected
admin-status: up
<source>
Source: NE-A
<destination>
Destination: NE-A
<src-tp-id>
Source-ttp: NULL
<dest-tp-id>
Destination-ttp: NULL
<tunnel>
name: <Service-1 ref>
type: <p2p ref>
tunnel-id: <tunnel-1-id ref>
<primary-paths>
Name: <path A-ref>
<config>
type: explicit
<explicit-route-objects>
index: 0
e-r-usage: route-include-ero
type: link
link-index: <link2>
Index=1
e-r-usage: route-include-ero
Type=label
Label: <…>
Index: 2
e-r-usage: route-include-ero
type: link
link-index: <link4>
…
Label: <…>
MDSC
PNC1
PNC2
PNC3
<secondary-paths>
NULL
Issues:
If there are multiple-topologies, should the MDSC specify on which topology?
Link-index in ERO missing!
How to specify ODU label? (in ODU tunnel)
ODU tunnel: how to augment from TE Tunnel?
Is unnumbered link same as TP? (router-id + interface-id)
Looking at the picture the tunnel should be from NE1 to NE6
Notes: How to model the TP endpoint for the tunnel / Segment-tunnel? Segment tunnel depends on the view.
How is this different from single layer, single domain use case?
Why does topology need to be specified? The endpoints must be within the same topology, as this request is coming to PNC.
ODU augmentation example is part of single layer, single domain use case.
Link index, etc. for ERO can be augmented in the te-transport-model