## Slide 1: Initial Set of Questions
Single-domain/Single-layer Use Case(s)

## Slide 2: Reference Network Scenario
S1
S2
S3
S4
S6
S9
S10
S11
Transport domain
C-R1
C-R2
C-R3
IP domain
C-R5
C-R4

## Slide 3: Controlling Hierarchy
MDSC
IP PNC
IP Network Domain
Client Controller
Transport PNC
Transport Network Domain
CMI (initially out of scope)
IP MPI
(out of scope)
Transport MPI
(in the scope)

## Slide 4: Comments/Questions
Single-domain assumption: only one PNC
Single-layer assumptions:
  All NEs are switching at the LO ODU level
    LO ODU multiplexing into HO ODU is not used or pre-configured (and not controlled at the MPI)
What type of topology abstraction? White, black or grey?
  Start assuming a white topology abstraction
  We can think later if we need also to analyze black or grey topology abstractions
What about client layer services?
  ODU transit service
  Other (non ETH) OTN client services (e.g., STM-N, FC, InfiniBand, …): single-layer or multi-layer?
  EPL over ODU: single-layer or multi-layer?
    Transparent versus frame-based mapping?
  EVPL over ODU: single-layer or multi-layer?
  Assumption: single-layer (no multiplexing/switching)
What about multi-function access link?
  To be addressed
  Assumption: single-layer (no multiplexing/switching)

## Slide 5: ODU Transit (ODU2)
S1
S2
S3
S4
S5
S6
S7
S8
Transport domain
C-R1
C-R2
C-R3
C-R5
C-R4
ODUk link
Note: OTN-Optical layer controlled by each domain controller and not exposed Via Controller NBI.
Traffic flow from C-R1 to C-R3:
C-R1 (PKT -> ODU2), S3 (ODU2), S5 (ODU2), S6 (ODU2), C-R3 (ODU2 -> PKT)
Note - C-R1 (PKT -> ODU2) and C-R3 (ODU2 -> PKT) adaptations not controlled by Transport PNC
S-LTP-3
S-LTP-6

## Slide 6: ODU2 Tunnel Setup
Abstract
Topology
@MPI
C-R1
C-R2
C-R3
C-R5
C-R4
MDSC should request Transport PNC to setup an ODU2 Tunnel (Segment) between S-LTP-3 and S-LTP-6
Ingress and egress points are indicated in the ERO of the primary path:
  First ERO element is S-LTP-3
  Last ERO element is S-LTP-6
  The tunnel to be setup is a segment tunnel, source and destination of the E2E tunnel
  information is belonging to customer side.
S-LTP-3
S-LTP-6
S3
S6
S1
S2
S4
S5
S7
S8

## Slide 7: ODU2 Connection: TEAS Tunnel Model Instantiation
ODU2 Connection
<te>
<tunnels>
<lsps-state>
<lsp>
src: 0.0.0.0
dest: 0.0.0.0
tunnel-id:1
lsp-id: ODU2-lsp-1-id
type: tunnel-p2p
lsp-oper-status: up
lsp-protection-role: working
<config>
name: ODU2-Service-1
identifier: 1
type: tunnel-p2p
bandwidth: 10Gbps
lsp-prot-type: unprotected
admin-status: state-up
<tunnel>
name: <ODU2-Service-1 ref>
identifier: <1>
<p2p-primary-paths>
<config>
type: explicit
<state>
type: explicit
<lsp>
<lsp-ref>
<lsp-record-route>
<explicit-route-objects>
index: 0
e-r-usage: route-include-ero
type: unnumbered-link
S3
-LTP 3 ??
<rro>
subobject-index: 0
Router-id: ??
Interface-id: ??
<te>
<tunnels>
<primary-paths>
Config Datastore
Operational/State Datastore
<explicit-route-objects>
index: 1
e-r-usage: route-include-ero
type: unnumbered-link
S6
S-LTP-6
<rro>
subobject-index: 0
Router-id: ??
Interface-id: ??
1) Not clear how to get information about the router-id and interface-id from the TE topology
2) Not clear how to use the label to identify the spcecific ODU2
<config>
name: ODU2-Service-1
identifier: 1
type: tunnel-p2p
bandwidth: 10Gbps
lsp-prot-type: unprotected
admin-status: state-up
Oper-status
<tunnels>
Reverse direction
Could we use the explicit-route-usage attribute to identify the ERO representing the incoming and outgoing ports from the domain?

## Slide 8: ODU2 Connection: TEAS Tunnel Model Instantiation - alternative
ODU2 Connection
<te>
<tunnels>
<lsps-state>
<lsp>
src: 0.0.0.0
dest: 0.0.0.0
tunnel-id:1
lsp-id: ODU2-lsp-1-id
type: tunnel-p2p
lsp-oper-status: up
lsp-protection-role: working
<config>
name: ODU2-Service-1
identifier: 1
type: tunnel-p2p
bandwidth: 10Gbps
lsp-prot-type: unprotected
admin-status: state-up
<tunnel>
name: <ODU2-Service-1 ref>
identifier: <1>
<p2p-primary-paths>
<config>
type: explicit
<state>
type: explicit
<lsp>
<lsp-ref>
<lsp-record-route>
<explicit-route-objects>
index: 0
e-r-usage: incoming-ero
type: unnumbered-link
S3
-LTP 3 ??
<rro>
subobject-index: 0
Router-id: ??
Interface-id: ??
<te>
<tunnels>
<primary-paths>
Config Datastore
Operational/State Datastore
<explicit-route-objects>
index: 1
e-r-usage: outgoing-ero
type: unnumbered-link
S6
S-LTP-6
<rro>
subobject-index: 0
Router-id: ??
Interface-id: ??
1) Not clear how to get information about the router-id and interface-id from the TE topology
2) Not clear how to use the label to identify the spcecific ODU2
<config>
name: ODU2-Service-1
identifier: 1
type: tunnel-p2p
bandwidth: 10Gbps
lsp-prot-type: unprotected
admin-status: state-up
Oper-status
<tunnels>
Reverse direction
Could we use the explicit-route-usage attribute to identify the ERO representing the incoming and outgoing ports from the domain?

## Slide 9
In this scenario the tunnel is not terminate in the OTN NW, it is a «Transit tunnel» , starting from router side
How can we get information regarding the ingress and egrees point of the transit tunnel (router-id and interface-id) ?
  The router id can be the te-node-id in the teas-topology
  The interface-id can be the te-tp-id in the teas-topology
The same problem appear for lsp-state part with RRO
Action (Sergio) – Check with TE Tunnel model experts for clarification
How the specific ODU2 (e.g., TS information) to be used on the access links is configured
  Some negotiation process is needed
  It may depend on how this information is selected:
    If selected by the NE/PNC, it is communicated by the PNC to the MDSC after the Tunnel has been setup
    If selected by others (e.g., MDSC), it should be communicated by the MDSC in the ERO elements when the Tunnel setup is requested
  Current assumption: the MDSC selects the specific ODU2
If MDSC selects the ODU2 to be used on the access link it is not clear how it could get the information about the available TSs among which it can select
  Possible conclusion: it is beneficial not to advertise the available BW in terms of number of containers but we advertise which particular container is available. This information may be needed only for Tunnel configuration while for path computation this information is not needed.
Action (DT) – Continue to investigate this open issue

## Slide 10: Other OTN client services (STM-64)
S1
S2
S3
S4
S6
S9
S10
S11
Transport domain
C-R1
C-R2
C-R3
C-R5
C-R4
STM-N/FC/IB/… link
Traffic flow from C-R1 to C-R3:
C-R1 (PKT -> STM-64), S3 (STM-64 -> ODU2), S6 (ODU2), S9 (ODU2 -> STM-64), C-R3 (STM-64 -> PKT)
Note - C-R1 (PKT -> STM-64) and C-R3 (STM-64 -> PKT) adaptations not controlled by Transport PNC
ODU link

## Slide 11: EPL over ODU Services (10GE)
S1
S2
S3
S4
S6
S9
S10
S11
Transport domain
C-R1
C-R2
C-R3
C-R5
C-R4
10GE link
Traffic flow from C-R1 to C-R3:
C-R1 (PKT -> ETH), S3 (ETH -> ODU2), S6 (ODU2), S9 (ODU2 -> ETH), C-R3 (ETH-> PKT)
Note - C-R1 (PKT -> ETH) and C-R3 (ETH-> PKT) adaptations not controlled by Transport PNC
ODU link

## Slide 12: EVPL over ODU Services
S1
S2
S3
S4
S6
S9
S10
S11
Transport domain
C-R1
C-R2
C-R3
C-R5
C-R4
10GE link
Traffic flow from C-R1 to C-R3:
C-R1 (PKT -> VLAN), S3 (VLAN -> ODU0), S6 (ODU0), S9 (ODU0 -> VLAN), C-R3 (VLAN-> PKT)
Note - C-R1 (PKT -> VLAN ) and C-R3 (VLAN -> PKT) adaptations not controlled by Transport PNC
ODU link

## Slide 13: Multi-function access link
S1
S2
S3
S4
S6
S9
S10
S11
Transport domain
C-R1
C-R2
C-R3
C-R5
C-R4
Multi-function access link
10GE link
STM-64 link
ODUk link

## Slide 14: Multi-function access link
When C-R3 is connected with C-R1:
  C-R3-S9 access link is configured as a 10GE link
  Traffic flow from C-R1 to C-R3:
  C-R1 (PKT -> ETH), S3 (ETH -> ODU2), S6 (ODU2), S9 (ODU2 -> ETH), C-R3 (ETH -> PKT)
When C-R3 is connected with C-R4:
  C-R3-S9 access link is configured as an ODUk link
  Traffic flow from C-R4 to C-R3:
  C-R4 (PKT -> ODU2), S3 (ODU2), S6 (ODU2), S9 (ODU2), C-R3 (ODU2 -> PKT)
When C-R3 is connected with C-R5:
  C-R3-S9 access link is configured as a STM-64 link
  Traffic flow from C-R1 to C-R3:
  C-R5 (PKT -> STM-64), S3 (STM-64-> ODU2), S6 (ODU2), S9 (ODU2 -> STM-64), C-R3 (STM-64 -> PKT)
Note - C-R1 (PKT -> ETH), C-R4 (PKT -> ODU2), C-R5 (PKT -> STM-64), C-R3 (ETH -> PKT) , C-R3 (ODU2 -> PKT) and C-R3 (STM-64 -> PKT) adaptations not controlled by Transport PNC

## Slide 15: Backup

## Slide 16
S1
S2
S3
s36
S4
S6
S37
s38
S9
S10
S11
Network domain 1
S21
S22
S23
S25
S24
S26
S27
S28
S29
S30
S31
Network domain 2
C-R1
C-R2
C-R3
C-R4
C-R5
C-R6
Customer domain 1
Customer domain 2
Network domain 3
S39
Customer domain 3
C-R7
C-R8
ODUk link
Note:
OTN-Optical layer
controlled by each domain controller
and not exposed
Via Controller NBI.
Figure provided by Igor

## Slide 17: Controlling Hierarchy
MDSC
PNC1
PNC2
PNC3
Assumption:
1: client controller knows the C-Rx and its access link information.
2: MDSC knows how to map C-Rx and its network side of nodes within its network domain.
3: MDSC has no topology information at all before each PNC reports its topology.
Network Domain 1
Network domain 3
Network Domain 2
Client Controller

## Slide 18: Controlling Hierarchy – single domain
MDSC
PNC1
Network Domain 1
Client Controller
CMI: connectivity between C-R1 and C-R2
MPI: connectivity between C-R1 and C-R2
Single-layer use cases can cover both cases where there is only one network domain/PNC as well as multi-domain use cases where the connectivity request at the CMI is between access links attached to the same network domain
Assumptions:
CMI is the same: customer is not aware of whether the network or connectivity request is single or multi domain
MPI is the same: PNC is not aware of the existence of other PNCs